## Slide 1: Linear Power Supply
Team Sagittarius
Progress Review
2021 DEC

## Slide 2: Problem breakdown
We recognized 4 main requirements to complete the Linear Power Supply.

## Slide 3: Conversion stage
Our preferred solution

## Slide 4: Calculation of required values
1. Reducing the AC 230 V to a suitable value
2. Use a high-power full bridge rectifier to rectify
3. Use LC low pass filter to filter out the AC component
4. Filtered current is the base current for the 2N3904 transistor then it will provide a base current for the TIP141 Darlington transistor
5. Datasheets of these transistors show 10A collector current is possible
6. We have a very stable base current, a stable collector current also can be expected
7. Zener diode used to regulate to 13.8V because there will be a 2V drop at the BE.
8. Protection circuits needs this 11.8 minimum voltage is required to supply 10V after protection circuits.

## Slide 5: Simulation in Proteus
<Replace the image!!!!!!!!!>

## Slide 6: Selected Parts
The Darlington pair : TIP141 https://www.onsemi.com/pdf/datasheet/tip140-d.pdf
NPN BJT transistor : 2N3904 https://www.onsemi.com/pdf/datasheet/2n3903-d.pdf
Zener Diode : BZX79C15 https://datasheetspdf.com/pdffile/994603/TaiwanSemiconductor/BZX79C15/1
High power bridge rectifier
https://www.bc-robotics.com/shop/bridge-rectifier-50a-1000v

## Slide 7: Thank you!